LONDON / JANUARY 2020 / FOR IMMEDIATE RELEASE

Offering a new horizon for the yachting world, Philippe Briand’s SY200 design delivers a true sailing experience

on a 60-metre platform that is self-sufficient

in terms of energy requirements

Authenticity and a passion for performance are the core principles behind Philippe Briand’s new sailing superyacht concept, the SY200.

Summary presentation:

- The SY200 is the latest concept project from Philippe Briand.

- The equivalent power harnessed by the SY200’s sails is calculated to be 2,000kW, in optimum wind conditions.

- The SY200 would capture some of this kinetic energy through the movement of underwater turbines while sailing.

- The yacht would generate 500kW when sailing at 15 knots and 200kW at 12 knots, which would be sufficient to meet the onboard power demands of the hotel and manoeuvring systems while under sail.

- Philippe Briand’s motivation for designing the SY200 was to create a yacht that discharged zero emissions when travelling from port to port.

- Energy stored in the 20-tonne onboard battery bank would allow the yacht to be silently powered while at anchor.

- In order to achieve such impressive power generation while under sail, Philippe Briand’s renowned naval architecture expertise has been used to full effect through his high-performance hull design.

- The 200-foot sailing yacht has been devised to be the best performer in its category, and to deliver a sophisticated lifestyle on board.

- With the main living deck on one level, 80% of the yacht’s length is protected by a glass coachroof and hardtop. The immense skylight over this area gives an unobstructed view forward and upward to the sail and rig above.

- The interior features a totally revolutionary general arrangement, allowing more space for the four guest cabins and owner’s suite, which are particularly quiet and generously proportioned.

- The owner’s suite on the SY200 has direct, private access to the sea.

- Initial concepts of the yacht’s decor are based on the application of pure, raw materials and will be completed by the owner’s interior designer of choice.

- The SY200 has been designed to be under 500 gross tonnes, which minimises its weight and cost of maintenance.

Full presentation:

Philippe Briand has unveiled the latest sailing yacht concept to come from his London-based design studio: the 60-metre (200-foot) SY200. With a traditional sailing rig, the 490-gross-tonne sloop has been created to outperform the other sailing yachts under 499 gross tonnes that are on the water today, as well as to provide a head-turning aesthetic and ultimate comfort on board. The SY200 would be the ultimate prize possession for a passionate sailor who demands speed on the water as well as exceptional design and style.

A TRUE LEADER IN THE NEW WAVE OF “SUSTAINABLE ” SUPERYACHTS

Unlike the growing number of sailing superyachts that are effectively motor yachts with sails, requiring engines to assist in propelling them through the water, the SY200 is an authentic sailing yacht in all aspects. It has been developed with a similar design approach to that used in smaller, high-performance racing yachts while boasting the hallmarks of Philippe Briand’s award-winning design pedigree, including clean, dynamic lines and outstandingly efficient naval architecture.

Being fully wind propelled, the SY200 would be a true leader in the new wave of “green” superyachts; in particular, the hull form characteristics and predicted performance of the yacht would put it in pole position of this new category of yachts. In optimum conditions, a maximum speed of over 20 knots could be reached and the yacht’s remarkable hydrodynamic efficiency means more power could be harnessed through its underwater turbines to charge the batteries on board. Theoretically, if 50% of the energy is captured by the turbines, it would provide power equivalent to that of a 500kW generator, while maintaining a speed of around 15 knots.

Driven by the pursuit of efficiency rather than opting for a faddish design, Philippe Briand chose a sloop sailing rig to complement the contemporary hull with its slightly inverted bow, as this proves to be the most effective. With its foremast towering 83.5 metres above the waterline, the SY200’s upwind sail area is 2,000m2, while its downwind sail area is more than 3,000m2.

The design of the carbon fibre masts and rigging is heavily informed by the experience Philippe Briand acquired during the development and construction of the landmark 67m S/Y Vertigo and 73m S/Y Sybaris, two of the most celebrated sailing yachts in recent history.

SPECTACULAR DECK

The sailing yacht’s length at the waterline is 60m, with a maximum beam of 10.50m; although the design includes two spacious decks for ample guest space, Philippe Briand has been careful to ensure well-balanced proportions deliver a sleek overall aesthetic. This includes a spectacular glass coachroof on a completely flush deck. The star attraction of the exterior, the owner’s aft steering station, will be a magnet for friends and family to come together, where up to 14 guests can experience the uniquely thrilling sensation of movement created by harnessing the natural power of the wind.

Of course, full enjoyment of the SY200’s exterior can come at anchor or in port, as well as while cruising or racing. The uncluttered decks have a distinctly contemporary look and allow stunning vistas of the surroundings. An enormous 16-seat dining table in the cockpit, protected from the sun by the long hardtop, has superb panoramic views. The aft scope transom offers a large terrace over the sea and a private exterior space in direct communication with the owner’s suite.

INNER SPACE WITH REVOLUTIONARY SETTING

Instead of the traditional setting of the engine room amidships below the main guest accommodations, the SY200’s general arrangement presents a revolutionary setting: the engine room is located at a distance from the guest area, a third of the way back from the bow. The advantages are clear and many: there is a noise reduction in guest areas; there is easy access to the engine room from the crew quarters; there is more volume freed up amidships for the four large guest cabins; and with more weight placed forwards, this allows the possibility to move the keel and consequently the rig further aft for greater efficiency. The aft portion of the yacht is entirely dedicated to guest privacy, with a full-beam owner’s suite that leads onto a large terrace featuring a concealed Jacuzzi and direct access to the water.

Final interior layouts can be tailored to an owner’s desires but initial drawings of the SY200 allow provision for a large full-beam owner’s suite with his-and-hers bathrooms, an office and a private terrace on the main deck. A further four guest suites are located on the lower deck, as well as accommodation for up to 12 crew.

Philippe Briand commented on the announcement of the SY200 design:

“I have always expressed my faith in technology and efficiency, as they are an integral part of the yacht design process. Previously we designed sailing yachts for the express purpose – or the hidden purpose – of winning regattas, and so passionate owners pushed our industry to develop more and more high-tech sailing yachts. But this competitiveness is no longer an appealing motivation for today’s younger generation of yacht owners. As a result, the market for such advanced sailing yachts is dramatically down.

“I believe we need to embrace ‘lateral thinking’ when it comes to the future of sailing yacht design. We want to work alongside owners to create the perfect renewable energy machine, using only wind, water and solar energy to run the yacht and provide an exceptional experience of peace on board and exploration of the sea.

“Instead of using competition between owners as a motivator, environmental sustainability will become the reason to push the boundaries of technology and efficiency in superyachting. This is something we are very passionate about.”

Brief specs

Hull length			62.84 m

Hull beam			10.50 m

Waterline length		59.73 m

Draft				4.50/8.10 m

Air draft			83.90 m

Displacement			490 t

Upwind sail area		2000 mq

Downwind sail area		3700 mq

About Philippe Briand

London-based naval architect and yacht designer Philippe Briand has been conceiving high-performance, visionary yachts since his childhood days sailing in La Rochelle.

Today, Philippe Briand is the CEO and inspired team-leader coordinator of three design divisions: sailing yachts as Philippe Briand Ltd, motor yachts with Vitruvius Yachts Ltd and interiors by Philippe Briand – both for yachting and world-class real estate.

His technical excellence and precision, accompanied by a strong artistic flair and talent for fashioning innovative design trends in the yachting market, have continued to evolve over what is arguably the most prolific career of any yacht designer today.  Philippe Briand is one of the few real innovators in yachting, a “senior designer” of what is today the expedition/explorer vessels trend.

His successes have led him to build up a loyal client base of extremely discerning owners for custom designs, as well as to encourage a new generation of owners who are attuned to his prioritisation of sustainable, intelligent design solutions, efficient and long-range green technologies.

Briand’s background in naval architecture gives him the leading edge when it comes to integrating new technologies into his designs, as well as incorporating new materials or considering existing materials in new ways. His technical background and understanding of advanced hydrodynamics and production engineering have led to the creation of dozens of successful production yacht models over the years, accounting for over 12,000 vessels launched. The company’s current projects range from six to 105 metres, both for sailing yachts and motor yachts, including many highly customised and technical designs.

With offices in London and La Rochelle, France, Briand and his team of designers have won 34 international yacht design awards for their work (to date, Jan 2020), and have collaborated with some of the most highly respected sailing yacht builders in the world, including Perini Navi, Lürssen (Germany), Pendennis (UK), Royal Huisman (Netherlands), Vitters (Netherlands), CNB (France) and Groupe Beneteau (France).

PRESS OFFICE / SAND PEOPLE COMMUNICATION

sandpeoplecommunication.com

Elisa Corti

e@sandpeoplecommunication.com

m. +39 328 2478193